## Slide 1: Hydroacoustics And Field Computing
Tablet Usage for Hydroacoustics: Experiences and Lessons Learned

## Slide 2: Overview
Water Science Center Experiences
  Arin Peters – Hydrographer, KS WSC
  Kevin Housel – Hydrographer and field technical support, WI WSC
  Clinton Hittle – Pittsburg Field Office Chief, PA WSC
Summary of Options
  Jason McVay – HaWG regional representative - IA WSC
Open Discussion
  All presenters
  Burl Goree - Field Computing Integration and Support (FCIS)

## Slide 3: Convertible tablet PCs for field computing
Advantages over laptops:
Smaller
Lighter
Cheaper
More versatile
Battery life

## Slide 4: ASUS T100 Transformer

## Slide 5
Specs:
  Windows 8.1
  1.33 GHz atom Processor
  2.00 GB RAM
  32 GB Hard Drive
  Micro SD slot for added storage
  One USB 3.0 port in keyboard
  One Micro USB port (charging point) in tablet
  $350
ASUS T100 Transformer
Micro USB to USB adapter can be used if the keyboard is not connected or if you need to connect two devices

## Slide 6: Other Options:
Dell Venue 11 Pro
$499
Lenovo Miix 2
$499
HP Split x2
$799
Samsung ATIV Tab 7
$1199
Toshiba Portege Z10t
$1449

## Slide 7: Communicating with Acoustic Instrumentation/Gage house equipment
Spread Spectrum (SS) Radios using USB to Serial Adapter
Bluetooth

## Slide 8: Equipment used/communicated with
RDI RiverRay
Bluetooth and SS Radios
RDI StreamPro
Bluetooth
Son Tek Argonaut-SL (Side Looker) ADVM
USB to serial adapter
Sutron SatLink2 V2
USB to serial adapter
RDI Rio Grand 600kHz (and 1200kHz)
SS Radios

## Slide 9: Keeping your tablet dry

## Slide 10: WI-WSC Tablets
1st Generation Tablets
  HP Slate 500 8-inch
  ACER W500 10-inch
  Fujitsu 10-inch
2nd Generation Tablets
  Asus ME400C 8-inch
  Acer W3-810 8-inch
  Dell Latitude 10 – ST2 10-inch
Things you need to watch out for…
Pros
  Standard USB port
  SD Card Slot
  Processor Speed
Cons
  Non-dedicated power
  Real-estate

## Slide 11: WI-WSC Tablets
3rd Generation Tablets
  Panasonic ToughPad FZ-G1 10.1-inch
    2.40 GHz Intel Core i5
    128 GB Hard drive
    Win 8.1 64-bit OS
    8 GB Ram
    10.6’ HD screen (1920x1200)
  Microsoft Surface Pro2 10.6-inch
    1.70 GHz Intel Core i5
    128 GB Hard drive
    Win 8 64-bit OS
    4 GB Ram
    10.6’ HD screen (1920x1080)
  Dell Nevue 11 Pro 10.8-inch
    1.5 GHz Intel Core i5
    128 GB Hard drive
    Win 8.1 64-bit OS
    4 GB Ram
    10.8’ HD screen (1920x1080)
Pros
  Win 8/8.1
  Full Microsoft OS (must) USGS Field Software will not run on Microsoft RT
  Faster processor (min 1.5 GHz - Intel Core i5)
  Possible Desktop replacement w/ dual monitors requires docking station
    Full software field image allows on-site data processing (SiteVisit and GRSAT), using a MiFi or Smartphone HotSpot and eRAS.
    Can run all software, PCFF7.1, Sonutils, etc.
  Higher screen resolution allows software to “fit” better
Cons
  $$$
  Battery life
  Next Gen…
  Microsoft Surface Pro3?

## Slide 12: WI-WSC tablets

## Slide 13: Overall Pros and Cons from testing
Outdoor – viewable in sunlight
USB ports – std/micro adaptor cables for Parani’s
Internal BT support for other BT Devices, keyboard, etc.
  Platform dependent, may cause interference when using BT nubs, like AZIOs.
Portability, flexibility and versatility in mounts
Multi-function single USB port
  Charging uses same USB port
Processor speeds
  Higher speed with later models
OS limitations
  Hard Drive, min 120 GBs
Stylus
Keyboard functionality
Memory
Battery life

## Slide 14
Panasonic
CF-H2

## Slide 15
Panasonic CF-H2 Specs:
- Intel Core I5 1.7 gHz proc.
- 120 GB SSD drive
- 4-8 GB of RAM
- 64 Bit OS
- Class 1 bluetooth

## Slide 17
Digitizer Pens:
Pen sent with tablet is not good. Rugged digitizer pen
from Motion computing works well but does not fit
into the tablet. Buy spares because they are easy to
lose .

## Slide 18
The CF-H2 holds two batteries. Battery life is
average. Recommend purchasing spares.

## Slide 20
Internal Bluetooth option:
- Very good range.
- Connect to the instrument before
entering the software package.

## Slide 21
Sontek M9 has internal bluetooth

## Slide 24
RSL software:

## Slide 25
Panasonic CF-H2 Tips:
Disable bluetooth when not needed as it can
Interfere with other communications such as
communicating with an ADVM via serial.
Turn power save off while collecting discharge
measurement data.

## Slide 26: Hydroacoustics and Field Computing Webinar Summary
-We heard from three different users within the USGS using tablets while collecting Hydroacoustic data.
-All three are using different tablet platforms.
-Some of the reasons for making the change to a tablet are.
-Solo ADCP measurements
-Mobility
-Functionality – (ie. rugged, robust processing, replaceable)
-With the many options available for tablets there are trade-offs of cost, performance and durability. Each WSC will need to determine the option that works best for their situation.

## Slide 27: Summary of Tablet Options
Inexpensive and Portable – Processors and memory are less superior and tend to be used mostly for data collection and not used as a substitute for a full laptop or tablet. The processors for these tablets are usually Intel Atom (Bay Trail) processors.
Desired minimum specs:
  1280 x 800 resolution
  2 gigs of RAM
  32 gig hard drive (64 gigs preferred)
  ability to use USB port and charge the tablet at the same time. (preferred)
  Cost range: $300 to $700

## Slide 28: Summary of Tablet Options
Powerful and Non ruggedized– Processors and memory are more robust and could be used as a full laptop or desktop. Although this option would need to be protected in adverse weather.
Desired min. Specs for this option are:
  I3 or I5 processor
  4 to 8 gig RAM
  128 gig hard drive
  USB 3.0
  $700+

## Slide 29: Summary of Tablet Options
Powerful and Ruggedized– These tend to be fully ruggedized or mostly so, and have robust processors. The processor are typically I-3 or higher.
Desired min. Specs for this option are:
  I3 or I5 processor
  4 to 8 gig RAM
  128 gig hard drive
  USB 3.0
  Cost range : $2000 to $3500+

## Slide 30: Connectivity Options
Office:
  Docking station: tablet specific or universal USB 3.0 (approx $130)
    Gigabit Ethernet – for connecting to the network
    Additional USB ports
    Dual monitors
Field:
  Instrument commutations
    USB Serial port (FTDI chipset, available from HIF)
    Parani SD1000U - can be used as serial port and does not conflict with built-in bluetooth
    Long range (Class 1) Bluetooth USB
      may conflict with internal bluetooth. Which may mean that the internal bluetooth would have to be disabled.

## Slide 31: Sources of Information
Electronic Field Forms and Mobile Computing
  https//hydroacoustics.usgs.gov/forum
  This room is located on the OSW forum and is meant to be a location for users to share their experiences with mobile computing, ask questions, and archive previous discussions.
FCIS - Field Computing Integration and Support (FCIS)
  http://wwwrustla.er.usgs.gov/fcis/
  Covers all of the information regarding SWAMI, SWAMI PC, Station Levels, MONKES, and CHIMP
BWTST (NT_TAC) - Bureau Windows Technical Support
  http://bwtst.usgs.gov/
  Covers all of the current support related to the Windows operating system
OSW Hydroacoustics
  hydroacoustics.usgs.gov
  Covers all of the latest information regarding the use of Hydroacoustic equipment within the USGS. Including were to find the latest software and firmware versions of our most commonly used equipment.

## Slide 32: Questions?
There has been time set aside during this webinar for questions so please feel free to ask.
Thank you for attending.

## Slide 34: Open Discussion